## Slide 1: GROUNDWATER AVAILABILITY ASSESSMENT IN THE KUMI SUB-BASIN (EASTERN UGANDA)
JOHN ILIMA
MSCIV (Candidate)
College of Engineering, Design, Art and Technology
MAKERERE UNIVERSITY- KAMPALA.

## Slide 2: INTRODUCTION
Fresh water is a key strategic resource for Uganda’s economic development.
Key challenges:
Climate change impacts (droughts, floods,etc)
Water shortages
Quality deterioration
Skewed understanding on availability
Poor management
Kumi is already a victim of all these!
Policy Brief

## Slide 3: INTRODUCTION (cont’d)
Surface sources-more erratic
Groundwater-a critical resource in the area:
Reliance for daily supply has grown exponentially-rapid extraction campaign
Sustainability- a key concern
Hydrogeological conditions and behavior of watershed is not well understood.
Policy Brief

## Slide 4: METHOLOGY
A 90 m resolution Digital Elevation Model geo-referenced and processed in ArcGIS 10.1 to delineate the basin.
Policy Brief
Figure 1: Kumi Sub-basin

## Slide 5: METHOLOGY
Meteorological, lithological, groundwater level and pumping test data were collected, synthesized and analyzed to prepare various model inputs.
Recharge flux was estimated using Chloride Mass Balance (Bear & Verruijt, 1987)
Conceptual model constructed prior to numerical modeling.
Policy Brief

## Slide 6: METHOLOGY
A steady-state numerical groundwater model developed and calibrated using PMWIN 5.3 (Chiang & Kinzelbach, 1998).
Sensitivity analysis of the model carried out.
Policy Brief

## Slide 7: FINDINGS
Kumi aquifer system is of fractured-rock type average transmissivity of 5.12 m2/day.
Policy Brief

## Slide 8: FINDINGS (cont’d)
Groundwater flows towards the central plain of the basin, with resultant discharge being to the southwest.
Policy Brief

## Slide 9: FINDINGS (con’t)
Average recharge ranges 74-126 mm/year representing about 6-10% of average annual rainfall.
Model more sensitive to transmissivity and recharge. And more sensitive to recharge reduction than increment.
Policy Brief
Chart: Recharge Factor
| 0.5 | 0.70000000000000007 | 0.9 | 1 | 1.1000000000000001 | 1.3 | 1.5
RMSE | 135 | 72 | 19.4 | 4 | 5 | 10.4 | 20
MAE | 125 | 65 | 19.2 | 4 | 4.8 | 10 | 23
ME | 125 | 69.6 | 19 | 4 | 4.5 | -6.6 | -15.4

## Slide 10: RECOMMENDATIONS
Focused studies on the geological structure and fissure system of basin be undertaken.
Techniques: VES, EM traversing, radon Gas surveys
Economically feasible methods to improve supply be developed and piloted.
Angled drilling & collector wells
Detailed study of the central reach of the basin, as a potential wellfield be undertaken.
Policy Brief

## Slide 11: END OF PRESENTATION
THANK YOU FOR LISTENING
Policy Brief